## Slide 1
Nonlinear Dynamics
_______________________________________
Bibliographic Study:
Nonlinear Vibrations and Chaos in Gongs and Cymbals
Ali Saqib
Shahariar Ryehan
Subarna Paudel
Timothy Nathaniel Gunawan
Author:
Antoine Chaigne
Cyril Touzé
Olivier Thomas

## Slide 2
1/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
Introduction
Summary of Experiments
Analysis & Discussion
Gongs and cymbals are “nonlinear percussion instruments” where the vibratory displacement is comparable to thickness, leading to strong geometric nonlinearity
Objectives:
Summarize experiments and theoretical equations of nonlinear, chaotic vibrations in gongs and cymbals to reproduce the main dynamical features of gongs and cymbals and serve as a foundation for realistic sound production and synthesis purposes.
Observed Nonlinear Features
Amplitude-dependent harmonics
Pitch Glide
Bifurcations & Energy exchange between modes
Chaos

## Slide 3
2/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
Introduction
Summary of Experiments
Analysis & Discussion
Excitation Method:
Sinusoidal electromagnetic force with slowly increasing amplitude (instead of a mallet impact) at frequencies near eigenmodes to simplify interpretation.
Experiment Setup
Results
Periodic Motion
1
2
3
First Bifurcation
The structure's acceleration exhibits a periodic motion with an increasing level of harmonics (2Ω, 3Ω, etc.). The vibration is largely dominated by the forced mode
Occurs at a given force threshold, explained by energy exchange between normal modes due to an internal resonance relationship.
Quasiperiodic Motion
Occurs between the first and second bifurcation, spectrum is enriched by new frequencies ().
with and
4
Second Bifurcation
The motion becomes chaotic (broadband spectrum)

## Slide 4
3/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
Theoretical Model & Formulation:
Why Quadratic (2) Dominates over Cubic (3)?
Flat Plates: Ideally, flat structures possess symmetry. This symmetry leads to Cubic nonlinearity
Gongs/Cymbals: These are Shallow Spherical Shells. The curvature breaks the symmetry of the vibration.
Result: This asymmetry activates the Quadratic nonlinearity
Mathematical Magnitude vs.
The relative strength of the nonlinear terms depends on the shell’s geometry:
Quadratic parameter:
Governing Equation & Nonlinear Effects
The response to sinusoidal excitation with linear viscous damping is:
Quadratic Term
Cubic Term
Introduction
Summary of Experiments
Analysis & Discussion

## Slide 5
4/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
Theoretical Model & Formulation:
MMS Setup
    Time scale , (slow)
    Expansions:
    Substitute & Separate:
    Removing Scaler Term
    Solution
    Plug in to , then create resonance.
    Solvability Condition :
Final Amplitude–Frequency Relation:
Frequency increases with Amplitude .
Nonlinear Normal Modes (NNM) Formulation
Concept: Extension of linear modes to the nonlinear regime.
Definition: A synchronous periodic oscillation where all material points reach equilibrium/extremum simultaneously.
Invariance Property: Motion initiated on the NNM manifold stays on it.
Energy Dependence: Unlike linear modes, NNM frequency depends on energy (E).
Representation: The Backbone Curve is essentially the projection of the NNM onto the Frequency–Energy plane.
Von Karman Equation
  Physical Origin: Thin plate(h<<R)
    Geometric Nonlinearity: stretching mid plane
    Strain Displacement:
    Von Karman PDE:
    Cubic Nonlinearity (Stretching
    Projection to ODE
    Goal : Convert PDE (x,t) to ODE (t) by ansatz and Galerkin method
    Result Duffing equation:
    Here is it’s a Hardening behaviour.
Introduction
Summary of Experiments
Analysis & Discussion

## Slide 6
Weakly Nonlinear Regime (Pitch Glide)
Pitch Glide only occurs when the nonlinearity is kept relatively weak (ex. thick gongs), but not on thin cymbals where
the nonlinearity is more pronounced and the energy transfer and mode coupling phenomena dominates.
5/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
Downward Glide
1
Upward Glide
2
Occurs in flat surface gong
Hardening behaviour, resonance curve is bent to the right (direction of increasing frequencies)
Governed by cubic nonlinearity
Occurs in smaller gong with a pronounced curvature
Softening behaviour, resonance curve is bent to the left
Governed by the balance between quadratic and cubic nonlinearity
Introduction
Summary of Experiments
Analysis & Discussion

## Slide 7
Weakly Nonlinear Regime (Nonperiodic Regime)
6/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
The rich, multitone sound of gongs and cymbals may be produced by the coexistence of stable subharmonics of order 2 with the forcing frequency.
Stability Curve (amplitude vs detuning factor)
1
System of 3 coupled NL oscillators arose from Karman eqn
Observed on twin asymmetric modes (6,0)a and (6,0)b
Use of method of multiple scales
Where,
solid: stable
dashed: unstable
Introduction
Summary of Experiments
Analysis & Discussion
Amplitude of high note drop and amplitude of low subharmonic notes explodes upward

## Slide 8
Chaos Analysis & Quantification
7/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
Phase Space
Correlation Dimension
Lyapunov Exponent
Transition to chaos when amplitude is increased:
Periodic → Quasiperiodic → Chaotic
The estimated correlation dimension quickly saturates to a finite value as the embedding dimension increases, indicating a strange (fractal) attractor of limited dimension, which is a sign of the chaos
The Lyapunov exponent quantifies chaos by measuring how rapidly nearby trajectories diverge in phase space, with a positive exponent indicating a chaotic behavior.
Introduction
Summary of Experiments
Analysis & Discussion

## Slide 9
Replication of Work
Spectrogram and cymbal response from a crash cymbal audio signal
8/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
Replication of the gong vibration eigenmodes from the paper
Analytical (Linear Eigenmodes)
Lab Measurement (Nonlinear Eigenmodes)
Introduction
Summary of Experiments
Analysis & Discussion

## Slide 10
Replication of Work
Chaos analysis
Background
Methodology
Analysis & Discussion

## Slide 11
The nonlinear coupling mechanisms responsible for the characteristic sounds of cymbals and gongs, using thin shallow spherical shells as an analogue and indicating that the same approach can be extended to more complex geometries, provided their coupling coefficients are computed numerically.
1
Both experimentally and theoretically, shows that energy transfer between modes is driven by quadratic nonlinearity due to shell curvature and is governed by precise frequency rules, with only a limited number of degrees of freedom needed to produce the observed instabilities.
2
3
Conclusion
Estimations of attractor dimension and Lyapunov exponents confirm that strongly excited gongs and cymbals exhibit chaotic dynamics.
9/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals

## Slide 12
1
[3] C. Touze´ and A. Chaigne, ‘‘Lyapunov exponents from experimental time series: application to cymbal vibrations,’’ Acustica - Acta Acustica, 86, 557–567 (2000) (slide 8)
2
3
Bibliography
[8] O. Thomas, C. Touze´ and A. Chaigne, ‘‘Nonlinear vibrations of free-edge thin spherical shells: modal interaction rules and 1:1:2 internal resonance,’’ Int. J. Solids Struct., 42, 3339–3373 (slide 3 )
10/10 Nonlinear Vibrations and Chaos in Gongs and Cymbals
[12] A. H. Nayfeh and D. T. Mook, Nonlinear Oscillations (Wiley, New York, 1979) (slide 4)